## Slide 1
Schedule + State
Simulator (State Predictor)
Scheduler
Scenario (Arrivals/Departures)
World State
World Simulator
Uncertainty Model
Uncertainty Model
The “World”
The Controller
Scheduling
Loop
The scheduling loop happens every T1 time units. The scheduling window, T2, defines how far in the future the scheduler assigns times to events. These are not the same.
The world uncertainty model approximates the behavior of the world. It is used to test schedule robustness.
The scheduler uncertainty model approximates the world uncertainty model. It is used to generate robust schedules.

## Slide 2
(aa4, G34, 4R, 0700)
(ua39,G2, 3L, 0730)
…
(sa32,G15, 3C,2100)
Un-serviced requests (scenario)
s1
sw1
Past
Now
4r
2c
s1
Unscheduled Future
Scheduled Future
Time 0
Schedule
Schedule Horizon
System Snapshot
2c
Flex horizon

## Slide 3
Definition of Conflict: Two aircraft occupy same position at same time.
Solution: Delay one of the aircraft at previous location.
Note: Inserting delays might cause other conflicts, either forward or backward in time.

## Slide 4
1
0
2
3
4
5
Simple Example:
3 gates (0,1,2).
1 runway: 5
Travel times on links
Scenario:
(aircraft, gate, release time)
(Red, 2, 6)
(Green, 1, 0)
(Blue, 0, 0)
Scheduling with conflict detection and resolution
Format: Time n: {(aircraft, locations)}
Time 0: (Blue,0), (Green,1)
Time 3: (Blue,3), (Green, 3) Conflict
Time 1: (Green,1) (Delay Green at previous location)
Time 4: (Green,3)
Time 6: (Red, 2)
Time 8: (Blue, 4)
Time 9: (Red,4), (Green,4) Conflict
Time 7: (Red,2) (Delay Red at previous location)
Time 10: (Red, 4)
Time 13: (Blue, 5)
Time 14: (Green, 5)
Time 15: (Red,5)
5
5
3
3
3
Predefined Routes
Blue: 0,3,4,5
Green: 1,3,4,5
Red: 2,4,5
Final Schedule
Format: flight: {(location, time)}
Blue: (0,0),(3,3),(4,8),(5,13)
Green: (1,1),(3,4),(4,9),(5,14)
Red: (2,7),(4,10),(5,15)
This schedule is optimal for the scenario. Total delay time: 2; makespan: 15
INPUTS

## Slide 5
1
0
2
3
4
5
Example 2:
3 gates (0,1,2).
1 departure runway: 5
1 arrival runway: 6
Scenario:
(dep/arr, aircraft, gate, dep/arr time, route)
(dep, Red, 2, 2, R)
(dep, Green, 1, 1, G)
(dep, Blue, 0, 0, B)
(arr, Orange, 0, 2, O)
(arr, Yellow, 2, 4, Y)
(arr, Brown, 1, 6, N)
Predefined Routes:
R: 2,4,5; O: 6,7,3,4,2
G: 1,3,4,5 Y: 6,7,8,9,3,1
B: 0,3,4,5 N: 6,7,8,9,3,0
5
5
3
3
3
6
7
2
8
8
9
4
2
5
Is there a conflict-free schedule that is
a delay-free schedule? What is it?
What is its makespan?
How ‘tight’ is the best schedule?
(That is, how much delay can it tolerate?)
R 2,2; 4,5; 5,10
G:1,1; 3,4; 4,9; 5,14
B:0,0; 3,3; 4,8; 5,13
O:6,2; 7,10; 3,12; 4,17; 2,20
Y:6,4; 7,12; 8,16; 9,18; 3,23; 1,26
N:6,6; 7,14; 8,18; 9,20; 3,25; 0,28
Notes: R 2,2; 4,5; 5,10
G:1,1; 3,4; 4,9; 5,14
B:0,0; 3,3; 4,8; 5,13
O:6,2; 7,10; 3,12; 4,17; 2,20
Y:6,4; 7,12; 8,16; 9,18; 3,23; 1,26
N:6,6; 7,14; 8,18; 9,20; 3,25; 0,28

## Slide 6
%
Conflicts
%
Conflicts
Schedule Tightness
Degree of Uncertainty
No re-planning
Different amounts of re-planning
No uncertainty
Some uncertainty
TEST 1. In this test we will fix the amount of re-planning performed, including no re-planning. The goal is to measure the effects of schedule tightness on amount of conflicts for varying degrees of uncertainty.
TEST 2. In this test we will fix the schedule tightness and measure the effects of uncertainty on the amount of conflicts for varying amounts of re-planning.
Note: All curves are hypothetical for the purpose of illustration only.